## Slide 1
INITIAL DIRECTION • SUPERVISOR DISCUSSION
Driver Drowsiness Detection
and Intelligent Road Safety
Assistance System
Objective
Develop a real-time, non-intrusive system to detect driver drowsiness and provide timely safety alerts or assistance.
Driver
Camera / Sensors
Drowsiness
Detection
Risk
Assessment
Alert / Safety
Assistance
Current understanding — sensing method and architecture remain open for discussion.
01
Notes: Confirm that this is the intended project objective before discussing implementation.
Emphasize that the sensing method and architecture have not been finalized.
[Sources]
- Teacher-provided reference PDF, summarized in the referenced conversation: high-level vision-to-risk-to-alert system logic.
[/Sources]

## Slide 2
INITIAL DIRECTION • SUPERVISOR DISCUSSION
Vision-based is a practical starting point
02
Approach | Typical input | Initial observation
Vehicle-based | Steering, lane, vehicle signals | Requires access to vehicle data
Physiological | EEG, ECG, EOG | More direct, but needs added sensors
Vision-based | Camera, face, eyes, mouth, head | Non-intrusive and easy to prototype
Hybrid | Multiple sensing modalities | Potentially robust, but more complex
Initial direction
VISION-BASED
Accessible
Camera data is easy to obtain
Non-intrusive
No wearable sensor burden
Prototype-ready
Suitable for real-time testing
Initial direction only — subject to supervisor feedback and further investigation.
Notes: Use the comparison to explain why vision-based monitoring currently appears practical.
State explicitly that the choice is not final.
[Sources]
- Teacher-provided reference PDF, summarized in the referenced conversation: vehicle-based, physiological, vision-based, and multimodal method categories; non-intrusive advantages of vision-based monitoring.
[/Sources]

## Slide 3
INITIAL DIRECTION • SUPERVISOR DISCUSSION
Possible vision-based direction
03
A candidate flow — the specific features and models are still open.
Camera /
Video
Face & Feature
Extraction
Visual
Cues
Temporal
Analysis
Drowsiness State /
Risk Level
Alert / Safety
Assistance
Candidate visual cues
Eyes
Eye closure, blink duration, PERCLOS
Mouth
Yawning
Head
Pose and nodding
Other behaviours
Distraction, e.g. phone use
Candidate architecture — features and models have not been finalized.
Notes: Explain that drowsiness should be assessed over time rather than from one frame.
Mention eyes, mouth, head movement, and distraction only as candidate cues.
[Sources]
- Teacher-provided reference PDF, summarized in the referenced conversation: facial/behavioural cues, temporal aggregation, risk estimation, and alerts; combination of geometric features and deep-learning detection in the reference implementation.
[/Sources]

## Slide 4
INITIAL DIRECTION • SUPERVISOR DISCUSSION
Key challenges & possible focus areas
04
Vision-based challenges
Challenge | Why it matters
Lighting | Face / eye detection may become unstable
Glasses & occlusion | Eye information may be unavailable
Head pose | Facial geometry changes
Individual differences | Fixed rules may not fit every driver
Generalization | Performance may drop for unseen drivers
Real-time performance | Detection and warning must be timely
Possible focus 1
Individual differences
Different drivers may need different thresholds or models.
Possible directions
Personal calibration • Adaptive thresholds • Subject-independent evaluation
Possible focus 2
Real-time performance
Accuracy alone is insufficient if detection or warning is delayed.
FPS • Processing latency • Detection latency • Hardware • Accuracy–speed trade-off
These are possible priorities for discussion — not finalized project contributions.
Notes: Invite feedback on whether individual differences and real-time performance are appropriate priorities.
Distinguish a research-oriented contribution from a complete-system contribution.
[Sources]
- Teacher-provided reference PDF, summarized in the referenced conversation: illumination, occlusion, head pose, individual differences, generalization, and real-time deployment challenges; lightweight inference and latency optimizations in the reference implementation.
[/Sources]

## Slide 5
INITIAL DIRECTION • SUPERVISOR DISCUSSION
Questions for discussion
05
The meeting should clarify scope, contribution, and the final success criteria.
01
Project scope
Is camera-based vision the intended main direction, or should we also consider vehicle or physiological signals?
02
Technical expectation
Should we train our own AI model, or may we use pretrained and feature-based methods?
03
Main project focus
Should we solve one technical challenge, or build a complete real-time system?
04
Safety assistance
Are warnings and risk-level alerts sufficient, or are additional assistance functions expected?
05
Success criteria
What would a successful final demonstration look like?
Desired outcome: confirm the direction before finalizing the architecture.
Notes: Prioritize questions 3 and 5 if discussion time is limited.
Use the answers to decide whether the project is research-oriented or system-oriented.
[Sources]
- Discussion questions synthesized from the project brief and the prior supervisor-meeting planning conversation; no external factual claims.
[/Sources]